## Slide 1
Intro to APRS
Presented by Tim Watson KB1HNZ
& Ryan Michaelson KB1YTR

## Slide 2
What is APRS?
APRS is short for Automatic Packet Reporting System – an amateur radio communications system for relaying real-time digital information that can be received locally and is also ingested into the APRS Internet System (APRS-IS), which is distributed globally for immediate access.
The system is based on the AX25 Packet protocol, and was developed by Bob Bruninga WB4APR, a senior research engineer at the United States Naval Academy.

## Slide 3
Bruninga implemented the earliest ancestor of APRS on an Apple II computer in 1982. This early version was used to map HF Navy position reports.
In 1984, Bruninga developed a more advanced version using a Commdore VIC-20 to report the position and status of horses in a 100-mile endurance run.

## Slide 4
During the next couple of years, Bruninga continued to develop the system, which was then called the Connectionless Emergency Traffic System (CETS).
Following a series of FEMA exercises throughout the 1990’s, the system was ported to IBM PCs, and the Automatic Position Reporting System evolved into its current form.
Now, with GPS technology more widely available, the term Position has been replaced with Packet to better describe the capabilities of the system and to emphasize its uses beyond mere position reporting.

## Slide 6
Worldwide APRS Frequencies
APRS is a local RF network.
Since 1997, however, it is integrated with a worldwide transparent internet backbone.
APRS provides universal connectivity, permitting ANY number of stations to exchange information just like voice users would on a voice net. Its not a “connected” network.
APRS can be used over ANY 2-way radio communications system.

## Slide 7
APRS Paths – n-N Paradigm

## Slide 8
APRS Paths – Radio Setup
Here’s an example of the Path setup on a Kenwood D710:

## Slide 9
APRS is not just position reporting!
Communications include Announcements, Bulletins, Messages, Alerts, Weather, and map elements such as Objects, Frequencies, Satellites, Nets, Meetings, etc.
Voice Alert - In 2001 an idea was introduced to set a CTCSS (100 Hz) tone to the monitored frequency so if someone is in simplex range and wants to make a call, they could do so by using a PL of 100Hz. By your radio up this way, you don’t have to always drive around with the volume turned down (Its actually recommended that you don’t). The speaker will still be quiet until someone makes a call.
Suggested Radio Setup:
CH1 "APRS va " . 144.39 CTCSS 100 . . <== normal APRS Voice Alert operation CH2 "APRSmute" 144.39 DCS XXX . . . <== To keep speaker QUIET even with other VA's nearby CH3 "APRS raw" 144.39 no tones . . . . . <== for listening to the raw channel CH4 "APRSinpt" . 144.39 no tones +600 <== For high reliability reception of event stations CH5 "APRSdigi" . 144.99 no tones. -600 <== For Temporary WIDE1-1 digi operation

## Slide 10
APRS & Weather
Weather has always been of particular interest to mobile operators. Any home APRS station with a weather instrument usually transmits his local weather conditions in his position packets.
They not only show the distance and bearing to the home weather station , but also the wind speed and direction, temperature and rain in the last hour. This is very handy for the distant traveler to see what the weather looks like in front of him.
In addition to home weather stations, National Weather Service warnings and watches are also transmitted on APRS for local users. These are transmitted as bulletins or messages.

## Slide 22
Resources - APRS.org

## Slide 23
APRS Compatible Devices

## Slide 24
Commercially Available Transceivers with APRS Capability

## Slide 25
Intro to APRS